# Standards Change Request

## File Checksums	SCR3-1034.v6

### Elizabeth D. Rye	May 15, 2006

#### Provenance:

Date: 2006-03-22, revision 5.0

Working Group: E. Rye (lead), T. King, M. McAuley

Title: File Checksums (SCR3-1034.v5)

Date: 2006-03-20, revision 4.0

Working Group: E. Rye (lead), T. King, M. McAuley

Title: File Checksums (SCR3-1034.v4)

Date: 2006-03-06, revision 3.0

Working Group: E. Rye (lead), T. King, M. McAuley

Title: File Checksums (SCR3-1034.v3)

Date: 2005-11-14, revision 2.0

Working Group: T. King (lead), M. McAuley

Title: MD5 Checksums (SCR3-1034.v2)

Date: 2004-11-22, revision 1.0

Working Group: J. Wilf (lead), T. King, M. McAuley

Title: MD5 Checksums for Files (SCR3-1034.v1)

#### Problem:

Provide a means for testing the integrity of PDS data.

As an entity responsible for maintaining data, it is critical that the PDS be able to ascertain the integrity of its archive.  This includes:

- verifying the integrity of data stored on various types of external physical media (all of which have finite life spans),

- detecting errors introduced during transfer of data to newer media,

- detecting errors that occur during the transmission of data from data providers to the PDS, between PDS nodes, from the PDS to the NSSDC, and from the PDS to end users.

#### Proposed Solution:

A simple method for detecting these types of errors is to create and maintain a list of checksum values for every file contained on a PDS archive volume (logical or physical).

The inclusion of this list as a file on a PDS archive volume, while optional, has the following advantages:

- It is consistent with the PDS policy of having all information necessary for an archive to be self-contained within that archive.

- It provides a simple mechanism to meet our obligation to enable the NSSDC to verify the integrity of the data they have received from us.

- It provides an incentive to data providers to generate the checksum values themselves.  This allows for an additional validation step to verify that the data the PDS receives from data providers has not been corrupted during transmission.

The proposal outlined in this SCR, while currently only permitting the MD5 checksum type, is not structurally limited to any particular type of checksum and should allow for the implementation of new and better checksum algorithms in the future.

The proposed changes outlined in this SCR are:

- Establish an optional, reserved file, "CHECKSUM.TAB" (or "axx_CHECKSUM.TAB" for multiple files), which contains checksum values for all files on an archive volume, to be included in the INDEX directory of the archive.

- Create a new keyword, CHECKSUM_TYPE, for use in the CHECKSUM.LBL (or axx_CHECKSUM.LBL) file, to allow for the future use of different types of checksums, should they become permitted.

- Update the element definition for the MD5_CHECKSUM keyword, updating the STATUS_TYPE to APPROVED.

#### Requested Changes:

Changes to the Standards Reference

The following changes to the PDS Standards Reference are required to support this SCR:

Add to section 10.2.2 Reserved File Names, "CHECKSUM.TAB".

Add to Chapter 19.3.2.3 INDEX Subdirectory, after INDEX.TAB:

CHECKSUM.LBL	Optional

This is the PDS label for the CHECKSUM.TAB file.  The column object description for the CHECKSUM column must contain the CHECKSUM_TYPE keyword.

Although CHECKSUM.LBL is the preferred name for this file, the name axx_CHECKSUM.LBL may also be used, with axx replaced by an appropriate mnemonic.

CHECKSUM.TAB	Optional

This file contains a checksum for every file on the volume except itself and any other checksum files and checksum file labels.  The format is to be a PDS ASCII tabular format, with two columns, one (named CHECKSUM) providing the checksum values and another (named FILE_SPECIFICATION_NAME) containing the path and name of each file in the archive relative to the root directory of the volume.

Although CHECKSUM.TAB is the preferred name for this file, the name axx_CHECKSUM.TAB may also be used, with axx replaced by an appropriate mnemonic.  For an example of the CHECKSUM.TAB and CHECKSUM.LBL files, see Appendix D, section D.2.

Each figure in Chapter 19.  Volume Organization and Naming, will need to be updated to include a “CHECKSUM.TAB” and a "CHECKSUM.LBL" file in the INDEX directory.

Appendix D, section D.2 add the sample CHECKSUM.TAB and CHECKSUM.LBL files as shown in the attachment.  (The following sections of Appendix D will need to be re-numbered.)

Changes to the Data Dictionary

Modify the description of the MD5_CHECKSUM keyword as shown in the attached element definition template.

Add the new keyword, CHECKSUM_TYPE, as shown in the attached element definition template.

Changes to the PDS Tool Suite

There are no changes needed to any PDS tool, because a number of utilities are already widely available which can be used to produce and read the CHECKSUM.TAB file.

#### Impact Assessment:

In addition to the above described changes, at some point checksum files will have to be generated for all archive volumes generated prior to the approval of this Standards Change Request.  Furthermore, each node will be responsible for developing tools to periodically validate the integrity of their archive holdings using the checksum files generated in response to this SCR.  Mechanisms may also be eventually generated (presumably associated with the product servers) to provide checksum values to users who download individual PDS data product files.

PDS_VERSION_ID                    = PDS3

LABEL_REVISION_NOTE               = "2004-04-06, CN: BAM;

2004-10-14, PPI: S. Joy; 2006-05-15, EN: EDR"

OBJECT                            = ELEMENT_DEFINITION

ELEMENT_NAME                    = "md5_checksum"

BL_NAME                         = "md5checksum"

DESCRIPTION                     = "

The MD5 algorithm takes as input a file (message) of arbitrary length

and produces as output a 128-bit 'fingerprint' or 'message digest' of

the input. It is conjectured that it is computationally infeasible to

produce two messages having the same message digest, or to produce

any message having a given prespecified target message digest.

Most standard MD5 checksum calculators return a 32 character

hexadecimal value containing lower case letters.  In order to accommodate

this existing standard, the PDS requires that the value assigned to the

MD5_CHECKSUM keyword be a value composed of lowercase letters (a-f) and

numbers (0-9).  In order to comply with other standards relating to the

use of lowercase letters in strings, the value must be quoted using double

quotes.

Example:  MD5_CHECKSUM = "0ff0a5dd0f3ea4e104b0eae98c87f36c"

The MD5 algorithm was described by its inventor, Ron Rivest of

RSA Data Security, Inc., in an Internet Request For Comments

document, RFC1321 (document available from the PDS).

References

==========

Rivest, R., The MD5 Message-Digest Algorithm, RFC 1321, MIT Laboratory for

Computer Science and RSA Data Security, Inc., April 1992."

GENERAL_DATA_TYPE               = "CHARACTER"

MAXIMUM                         = ""

MINIMUM                         = ""

MAXIMUM_LENGTH                  = "32"

MINIMUM_LENGTH                  = "32"

STANDARD_VALUE_TYPE             = "DEFINITION"

STANDARD_VALUE_SET_DESC         = "N/A"

KEYWORD_DEFAULT_VALUE           = "N/A"

UNIT_ID                         = "NONE"

SOURCE_NAME                     = "PDS CN/B. SWORD"

FORMATION_RULE_DESC             = "N/A"

SYSTEM_CLASSIFICATION_ID        = "COMMON"

GENERAL_CLASSIFICATION_TYPE     = "N/A"

CHANGE_DATE                     = "2006-03-20"

STATUS_TYPE                     = "APPROVED"

STANDARD_VALUE_OUTPUT_FLAG      = "N"

TEXT_FLAG                       = "N"

TERSE_NAME                      = "md5checksum"

SQL_FORMAT                      = "CHAR(32)"

BL_SQL_FORMAT                   = "char(32)"

DISPLAY_FORMAT                  = "JUSTLEFT"

AVAILABLE_VALUE_TYPE            = "N/A"

END_OBJECT                        = ELEMENT_DEFINITION

END

PDS_VERSION_ID                    = PDS3

LABEL_REVISION_NOTE               = "2006-05-22, EN: EDR"

OBJECT                            = ELEMENT_DEFINITION

ELEMENT_NAME                    = "checksum_type"

BL_NAME                         = "checksumtype"

DESCRIPTION                     = "

The CHECKSUM_TYPE keyword is used to specify the type of checksum

algorithm used to calculate a checksum for a file or data object."

GENERAL_DATA_TYPE               = "IDENTIFIER"

MAXIMUM                         = "N/A"

MINIMUM                         = "N/A"

MAXIMUM_LENGTH                  = "12"

MINIMUM_LENGTH                  = "1"

STANDARD_VALUE_TYPE             = "DYNAMIC"

STANDARD_VALUE_SET              = {"MD5"}

STANDARD_VALUE_SET_DESC         = "N/A"

KEYWORD_DEFAULT_VALUE           = "N/A"

UNIT_ID                         = "N/A"

SOURCE_NAME                     = "PDS EN/E. RYE"

FORMATION_RULE_DESC             = "N/A"

SYSTEM_CLASSIFICATION_ID        = "COMMON"

GENERAL_CLASSIFICATION_TYPE     = "N/A"

CHANGE_DATE                     = "2006-03-20"

STATUS_TYPE                     = "APPROVED"

STANDARD_VALUE_OUTPUT_FLAG      = "Y"

TEXT_FLAG                       = "N"

TERSE_NAME                      = "checksumtype"

SQL_FORMAT                      = "CHAR(12)"

BL_SQL_FORMAT                   = "char(12)"

DISPLAY_FORMAT                  = "JUSTLEFT"

AVAILABLE_VALUE_TYPE            = "N/A"

END_OBJECT                        = ELEMENT_DEFINITION

END

D.2  CHECKSUM.TAB and CHECKSUM.LBL

Each PDS archive volume should preferably include a "CHECKSUM.TAB" file in the INDEX subdirectory.  This file, when present, must be accompanied by a detached PDS label.  (Note that in the case of multiple checksum files in the same directory of an archive volume, the files may be named axx_CHECKSUM.TAB and axx_CHECKSUM.LBL respectively, where axx is replaced by an appropriate mnemonic.)  The CHECKSUM.TAB file contains a checksum for every file contained on the archive volume (or in the entire archive, if stored as a virtual volume online), with the exception of any checksum files themselves and their labels.

D.2.1  Example of CHECKSUM.TAB

1e8d45f622e09b9e2998af1a6d67a296 AAREADME.TXT 7dcfa51691ddd149a5a091ebe87b9bb1 ERRATA.TXT

f8dd7758cb5231c9e7817c4710d00b6e BROWSE/MARS/C1246XXX/I862934L.IMG d8b83365f5e117b9665181944889da3d BROWSE/MARS/C1246XXX/I862934R.IMG

.

.

.

D.2.2  Example of CHECKSUM.LBL

PDS_VERSION_ID               = PDS3

RECORD_TYPE                  = FIXED_LENGTH

RECORD_BYTES                 = 71

FILE_RECORDS                 = 3623

DESCRIPTION                  = "CHECKSUM.TAB provides a checksum for all

files included on this archive volume, with

the exception of the checksum file itself

and its label."

^CHECKSUM_TABLE              = "CHECKSUM.TAB"

OBJECT                       = CHECKSUM_TABLE

INTERCHANGE_FORMAT         = ASCII

ROW_BYTES                  = 71

ROWS                       = 3623

COLUMNS                    = 2

OBJECT                     = COLUMN

NAME                     = CHECKSUM

DESCRIPTION              = "The checksum of the indicated file."

CHECKSUM_TYPE            = MD5

DATA_TYPE                = CHARACTER

START_BYTE               = 1

BYTES                    = 32

END_OBJECT                 = COLUMN

OBJECT                     = COLUMN

NAME                     = FILE_SPECIFICATION_NAME

DESCRIPTION              = "Identifies the file for which the checksum

was calculated."

DATA_TYPE                = CHARACTER

START_BYTE               = 34

BYTES                    = 36

END_OBJECT                 = COLUMN

END_OBJECT                   = CHECKSUM_TABLE

END